## Slide 1: Estimation of a nonlinear system with Extended Kalman Filter and C4dynamics

## Slide 2: The nonlinear system
estimation of the ballistic coefficient () of a target is necessary for accurate track of ballistic targets
ballistic coefficient (): The ability of a body to overcome air resistance in flight
high = small drag
  mass
  aerodynamic coefficient of drag
  reference surface area
The equation of motion in one dimension (height) is given by:
Notes: Post 1: why ekf? The difference between linear and nonlinear.
What’s the punch?
None of the following systems could be developed: ..
Missile guidance, satellite navigation, autonomous driving, and much more could not have been developed without the support of extended Kalman filter estimation.
While the Kalman filter excels in linear systems, the EKF boldly extends its prowess to tackle the complexities of nonlinear systems, making it a dynamic force in modern estimation algorithms

## Slide 3: EKF - the process
State
  Height position
  Height velocity
  Ballistic coefficient
Dynamics
Noise
  uncertainty
Predict equations
Notes: The nonlinear part of the filter is manifested in the dynamic equations. These include the height velocity derivative which when expressed in terms of the ballistic coefficient is a nonlinear function of the height position , the height velocity , and the ballistic coefficient itself.
When the process noise matrix is time-varying, you can provide the predict function with it at each call.
The nonlinear part of the filter is manifested in the dynamic equations. These include the height velocity derivative which when expressed in terms of the ballistic coefficient 𝛽 is a nonlinear function of the height position 𝑧, the height velocity 𝑣_𝑧, and the ballistic coefficient 𝛽 itself.
When the process noise matrix 𝑄 is time-varying, you can provide the predict function with it at each call.

## Slide 4: EKF - the measure
Sensor
  Height position radar
Noise
  Measurement variance
Rate
  50msec
Update equations
Notes: The nonlinearity may be manifested in different ways.
The system equations and the measure equations must be linearized even for the case of the extended Kalman filter, for the calculations of P and k. but as opposed to the regular Kalman filter, they are not linearized once about an equilibrium state, but rather they are linearized at each step about the estimated state.
In fact not always both the process equations and the measure equations are both nonlinear, and there may be mixed situations, i.e. either the process equations nonlinear or the measure equations nonlinear. But if both the process equations are linear and the measure equations are linear, then the selection in extended klaman filter is basically a missunderstandning, and the effort to calculate the linearized matrices at each step is total useless.
transition matrix F and the measure must be linearized for the calculation of P at the predict stage.
If the system equations are nonlinear, then the transition matrix F is linearized about the current estimated step at each step.
But

## Slide 5: Predict & Update
Predict equations

## Slide 6: Predict & Update
Update equations

## Slide 7: C4dynamics
The Python Framework for Motion Estimation and Control
Datapoint
Rigidbody
Sensors
Detectors
Filters

## Slide 8: Target simulation
''' true target '''
tgt = c4d.datapoint(z = z0, vz = vz0)
tgt.beta = beta0 # balistic coefficient # main loop
for t in np.arange(0, tf, dt):
''' true target motion '''
fz = tgt.mass * (0.0034 * np.exp(-tgt.z / 22000) * c4d.g_fts2 * tgt.vz**2 / 2 / tgt.beta - c4d.g_fts2)
tgt.inteqm([0, 0, fz], dt)
tgt.store(t)

## Slide 9: Target simulation

## Slide 10: Radar simulation
radar_noise = c4d.sqrt(500) # 1 sigma
''' altitude radar '''
rdr = c4d.sensors.seeker(dt = 50e-3, rng_noise_std = radar_noise)
# main loop
for t in np.arange(0, tf, dt):
''' measure '''
rdrout = rdr.measure(tgt, t = t)

## Slide 11: Radar simulation

## Slide 12: Kalman Predict
Equations

## Slide 13: Kalman Predict
# nonlinear derivatives for x
fx = [tgt_trk.vz, rgvzb * tgt_trk.vz / 2 - c4d.g_fts2, 0]
x = [tgt_trk.z, tgt_trk.vz, tgt_trk.beta]
xout = tgt_trk.kalman.predict(x, fx = fx, F = Phi, Q = Q)

## Slide 14: Implementation
''' true target '''
tgt = c4d.datapoint(z = z0, vz = vz0)
tgt.beta = beta0 # balistic coefficient
''' measured target '''
tgt_trk = c4d.datapoint(z = tgt.z0 + 25, vz = tgt.vz -150)
tgt_trk.beta = tgt.beta + betaerr0
''' kalman '''
tgt_trk.kalman = c4d.filters.e_kalman(p0, dt = dt, H = H, Q = Q, R = R)
''' altitude radar '''
rdr = c4d.sensors.seeker(isideal = True, dt = 50e-3, rng_noise_std = radar_noise)
Both the true target (for reference) and the estimated target are simulated with c4dynamics’ datapoint

## Slide 15: Implementation
for t in np.arange(0, tf, dt):
''' true target motion '''
tgt.inteqm([0, 0, fz], dt)
tgt.store(t)
if tgt.z <= 0: break
''' predict '''
xout = tgt_trk.kalman.predict(x, fx = fx, F = Phi.tolist(), Q = Q)
''' measure & update '''
rdrout = rdr.measure(tgt, t = t)
if rdrout is not None:
xout = tgt_trk.kalman.update(x, rdrout[2])
tgt_trk.store(t)
With c4d The system matrices (Q, R) may be introduced once at initialization (for constant matrices) or at each call for predict() or update() (for time varying matrices)

## Slide 16
Target
  radar error 1 std

## Slide 17: Results
''' nominal '''
z0 = 100000
vz0 = -6000
betaerr0 = 300
Phis = 0 (Q = zeros)

## Slide 18
improving as alt descends.
High rate predicts don’t matter.

## Slide 19
results agree with the covariance matrix.

## Slide 20: Results
''' high alt '''
z0 = 200000
vz0 = -6000
betaerr0 = 300
Phis = 0

## Slide 21
not observable where no drag.
High rate predictions are slightly better

## Slide 23: Results
''' high error '''
z0 = 100000
vz0 = -6000
betaerr0 = 1000
Phis = 0

## Slide 24
Doesn’t converge.
highly depends on initial conditions!
High rate predicts are helpful to estimate before hitting the ground.
-> if our initial guess is bad high rate predictions help to converge faster the solution

## Slide 25
the filter does not even realize when it is broken!

## Slide 26: Results
''' process noise '''
z0 = 100000
vz0 = -6000
betaerr0 = 1000
Phis = 1000**2

## Slide 27
fairly quick convergence.
High rate predicts almost don’t matter
---

## Slide 28
results agree with the covariance matrix

## Slide 29: Results
''' nominal + process noise '''
z0 = 100000
vz0 = -6000
betaerr0 = 300
Phis = 300**2

## Slide 30
Non accurate steady state error.
The uncertainty reduced from 300 lb/ft2 to about 100 lb/ft2 of error.
more robust to initialization errors filter
no difference between prediction rates

## Slide 32: Summary